## Slide 1: SuMo (GP) Verification
Javier Garcia Ordonez, Application Engineer
Cedric Bujard, Mathematical Modeler

## Slide 2: Content
  Background
  Methods
  Results
  Next Steps / Ideas

## Slide 3: Background

## Slide 4: Background
OptiStim MicroScale Model
  investigate the influence of different geometrical & tissue parameters on scalp nerve excitability
  implement surrogate modelling techniques (global SA and UQ)
    adequate predictions
    validation of surrogate models
    development of SA and UQ pipelines
    assess convergence

## Slide 5: Methods

## Slide 6: Results

## Slide 7: Results – Norm20D
Norm20D
  current normalization was introduced – mishap, wasn’t necessary during initial geometric investigation, and wasn’t initially added when introducing thicknesses and conductivities
  reparameterization of nerve & electrode depths to be relative to SCT and LAT layers – all parameter combinations are now valid
  “fake” 20D – POSITION (e.g. relative nerve – electrode displacement) is not included
    position is hypothesized to have a very large influence on the predictions and thus not allow the model to capture the influence of the other parameters

## Slide 8: Results – Norm20D
Norm20D
  GP training (1000 LHS) cross-validation metrics
    AF MAE / RMSE: 67 / 119 (over ~650 mean value)
    GAF MAE / RMSE: 2.0 / 2.96 (over ~20 m.v.)
    e.g. MAE is ~10% for both
  GP test (100 LHS) yields suitable results
    correctly looking QQ plot (k=1.5)
    same MAE and good truth-prediction (sorted) match for the AF
    not so good for GAF
  a(n)res to be evaluated

## Slide 9: Results – Norm20D
Norm20D
  prediction curve comparison with 1D cross-sections
    reasonable fit overall
    GAF is generally better (with 95% CI area)
    some unreasonable “truth” evaluations – to be inspected

## Slide 10: Results – Norm20DPosition
Norm20DPosition
  current normalization was introduced – mishap, wasn’t necessary during initial geometric investigation, and wasn’t initially added when introducing thicknesses and conductivities
  reparameterization of nerve & electrode depths to be relative to SCT and LAT layers – all parameter combinations are now valid
  real 20D – position (e.g. relative nerve – electrode displacement) IS included
    position is hypothesized to have a very large influence on the predictions and thus not allow the model to capture the influence of the other parameters

## Slide 11: Results – Norm20DPosition
Norm20DPosition
  GP training (1000 LHS) cross-validation metrics
    AF MAE / RMSE: 104 / 186 (over ~XXX mean value)
    GAF MAE / RMSE: 5.6 / 8.8 (over ~xx m.v.)
    e.g. MAE is ~xx% for both
  GP test (100 LHS) yields suitable results
    correctly looking QQ plot (k=1.5)
    both AF & GAF look reasonable; test MAE for AF is lower than CV5
  a(n)res to be evaluated
  extremely high test-GAF values to be inspected

## Slide 12: Results – Norm20DPosition
Norm20DPosition
  prediction curve comparison with 1D cross-sections
    NB Im using comfort pulse – the recovery phase could be even more excitating than the 5x1ms, thus anodic excitation (POSITION = +14) is high

## Slide 13: Results – Norm20DPosition
Norm20D
  for comparison with Norm20DPosition

## Slide 14: Next Steps
  check abnormal train / test values
  check a(n)res values

## Slide 15: Conclusions – Evaluation Metrics
  fitting quality of the uncertainty
    …
  prediction accuracy
    MAE, RMSE of (test) residuals